## Slide 1: Optimisation in my research
Jeremy Watson

## Slide 2: Overview
My research has used optimisation in a number of ways:
  Distributed optimisation and control algorithms for power systems (main focus today)
  Linear Matrix Inequalities (LMIs) for control synthesis*
  Optimal power-flow in unbalanced low-voltage distribution networks*
  (*slides at the end if anyone is interested)

## Slide 3: Distributed optimisation / control
Main idea:
  each agent / device / system controls its own variables (typically state variables of that system which are also design variables of an optimisation problem)
  by low band-width, distributed communication with other local agents, these variables are updated until the global optimisation problem is solved.
  this can allow large-scale optimisation problems to be solved automatically by simple controllers at each device as opposed to solving the problem centrally at high computational cost and broadcasting the solution to each device.
  already used (wide range of applications) in industry, although not especially common.
  potential applications (mostly in the future) include coordination of UAVs, self-driving vehicle platoons, smart grid, etc.

## Slide 4: Distributed optimization / control
Research areas:
  Improving convergence rates and properties (e.g. ADMM is one of the best recent algorithms)
  Coping with enforced dynamics in each agent. Agents typically have their own application-specific dynamics which may not be easy to control.
  Cyber-security – what happens if one or more devices are adversely controlled or deliberating send false data?
  Coping with time delays and/or noise in communication
  Stochastic networks – i.e. random communication failures, etc. – what can the distributed
  Hybrid approaches using some form of reinforcement learning as well.

## Slide 5: Application to power systems
replace optimal power-flow and frequency control with distributed optimisation & control
each generator has a controller that guides its power setpoints to the (true) OPF setpoint, based on communication with neighbours.
not really needed in the power system of today, but potential for implementation in future grids / microgrids

## Slide 6: Intro to distributed optimisation / control
Consider a separable cost function for a network of agents
Constraint: at steady-state, each agent must have the same value of the state variable (this is called a consensus problem). Typically this is something like a market price or (scaled) power output, etc.
i = agent i
xi = state of agent i
V = set of agents
Fi(xi) = cost function of agent i
Communication network matrix

## Slide 7: Intro to distributed optimisation / control
KKT conditions for optimality
Results also exist for cost functions which are not strictly convex, but not in all cases and not with the same simplicity
Guaranteed stability & optimality!!

## Slide 8
Primal-dual secondary frequency control with delays
(IEEE Trans. Automatic Control 2024)
Results (IEEE 39 system) with 20ms communication delays
Traditional controller
Our proposed controller
Results (IEEE 39 system) with noisy measurements (SNR = 20dB)
Our proposed controller
Traditional controller
Idea: transform the communicated variables to
allow noise resistance + delay robustness
Transformations

## Slide 9
Distributed Averaging
Proportional-Integral
Controller
Distributed secondary control for hybrid AC/DC grids
(IEEE Trans. Control Systems 2021)
Case study
Traditional controller
Our proposed controller
Optimisation formulation
Idea: implement a similar form of distributed optimisation
on hybrid AC/DC power grids
System dynamics
Control + Optimisation
theory used to prove
stability and optimality

## Slide 10: Linear Matrix Inequalities
State-of-the-art linear control techniques are usually based on Linear Matrix Inequalities (LMIs), where the control gains are the solution to a linear optimisation problem. Examples:
  LQR (Riccati equations are LMIs)
  Model predictive control
  H-infinity, H2 control
  Passivity-based control
  Stability analysis
Further reading (if interested): https://web.stanford.edu/~boyd/lmibook/lmibook.pdf

## Slide 11
Data-driven control
(Trickett, PMAPS 2024)
Scalable microgrid control
(IEEE Trans. Smart Grid 2021)
Formulation
System
Performance
Formulation
System
Performance
Inverse optimal and passivity-based control
(Hallinan, IEEE CDC 2023)
Formulation
Performance
System

## Slide 12: Unbalanced optimal power-flow
Back in 2017, optimal power-flow for unbalanced networks was mostly unexplored.
Published in IEEE Trans. Sustainable Energy.
22% reduction in energy losses
Results
Less computational expense
Formulation
Convexified
constraints
Small approximation error
Case study